## Slide 1: Microwave Tracking Ground Station (MTGS)
Team Members: Clay Edwards Christian Ogburn Jared O’Shea Jusefs Saade Jordan West Ian Wolfe
Product Owner: Dr. Eduardo Rojas

## Slide 2: Introduction
Ground stations are a key part in satellite communications
  Global Connectivity
  Emergency Response
  Navigation and Mapping
  Commercial Applications (such as our STMGS)
  Space Exploration
Sirius XM SXM-8 Satellite

## Slide 3: Change of Product Scope
Our contingency plan has been put into full effect
No longer receiving any new parts
Using all hardware from old ground station, except…
  Manufacturing our own RF Block
  Using new SDR module (Pluto)
All software is new as well

## Slide 4: Design/Safety Considerations
General Project Constraints
Available components for this ground station are those in the ERAU WiDE Lab
Gain/Loss
Size
Meteorological/Geographic Conditions
RocketDish 2.4 GHz WiFi Antenna
Safety Considerations
Personal/Hardware safety concern:
  Never exceed voltage or amperage ratings

## Slide 5: Summary of Project
Our mission is to track and receive signals from an S-Band frequency satellite.
The system is composed of five subsystems: A mount, positioner, tracking software, antenna, and software-defined radio (SDR)
Our focus this semester is tracking, setting up arriving hardware for testing and testing existing hardware

## Slide 6: Project Timeline
SPRINT 1
Scope Change?
Parts
Early Software
RF Block Research
SPRINT 3
RF Block Manufacturing
Satellite Point & Track
Record signals
Demodulation
SPRINT 2
Full Scope Change
RF Block Design
Software Testing and Confirmation
Demodulation Research

## Slide 7: Scrum & Backlog Progress
Notes:
A lot of backlog changes and shifting due to scope change
Much better process with deadlines and assignments on every task
Some delays due to scope change causing large documentation changes
Trello app, very convenient for reminders

## Slide 8: Antenna RF Block Design
Objective: optimize signal reception by our antenna, to ensure high-quality communication.
Components: Low Noise Amplifier (LNA), Bandpass Filter, Circular Polarization.
S-Band Antenna
Circular Polarizer (90 deg shift)
Bandpass Filter
LNA
Incoming Signal
RF Block
SDR
To Do:
Analyze current antenna.
Perform RF Block design (polarizer, coupled-line filter) using Ansys, ADS.
Revise link budget

## Slide 9: Coupled-Line Bandpass Filter
2.2-2.5 GHz
Butterworth
6th Order
Substrates:
  Copper
  Rogers RO4003C
To be completed:
  Impedance matching using two stubs
  Review attenuation at stopband and revise as necessary
  Begin manufacturing this week

## Slide 10: Polarizer Prototype (Delay Line)
To be completed:
  Meet lead researcher to validate
    Try microstrip line approach
  Scale to project requirements
  Manufacture in next 2 weeks
Substrates:
  Copper
  Rogers RO4003C
Frequency:
  1 GHz

## Slide 11: Project Link Budget Analysis
Objective: ensuring reliable communication between satellite and ground station; calculating necessary signal strength and quality.
Key variables: TX && RX powers, gains, losses, and noise figures.
Prx = Ptx + Gtx + Grx - Ltx - Lrx - Lfs
Lfs = free space path loss = 20 log10( 4π (d ⁄ 𝛌))
LM = (Prx - RS) > 0
RS = receiver sensitivity
To Do:
RF Block && Antenna: Power, gain and loss using MATLAB.
Ensure reliable communication.

## Slide 12: SDR Testing/Software
Working on testing PLUTO SDR - experiencing issues with software compatibility
Software needed to adjust SDR settings and record signals
Currently using SDR# - Good UI with recording features
Turned down MATLAB due to time constraints

## Slide 13: Satellite choice and Modulation
We have chosen SXM 8 a Sirius XM satellite.
The modulation schemes for the XM satellites is Coded Orthogonal Frequency Division Multiplexing: Differential Quadrature Phase Shift Keying (COFDM-DQPSK)

## Slide 14: What is COFDM?
COFDM is the division of one digital signal across 1000 other digital carriers simultaneously
The signals are sent at right angles from each other to avoid interference
COFDM applies Forward Error Correction (FEC)

## Slide 15: What is DQPSK?
Quadrature Phase Shift Keying (QPSK) enables transmission of two bits per symbol.
DQPSK encodes data based on the phase difference between consecutive symbols.

## Slide 16: Goals for Demodulation
Currently there is access to two different different pieces of Matlab code that can be used to demodulate COFDM and DQPSK.

## Slide 17: Tracking Software
Tracking Software outputs azimuth and altitude (elevation)
Starting with geostationary to test pointing, then moving to tracking
Ham tracking hardware and software
Python program for checking and testing within 0.0005 arcseconds of the Astronomical Almanac from the United States Naval Observatory

## Slide 18
For the tracking demonstration video, follow this link:
https://drive.google.com/file/d/1gMnMoOf3_ebvtcW9oFH6QjS_HROSX8R5/view?usp=sharing

## Slide 19: Lessons Learned
Verify datasheet consistency
Plan for budget changes
Plan for non-ideal conditions and parameters
Demodulation is very extensive and will take considerable research to do
Signal file format will be very important when it comes to determining the tracked signal

## Slide 20: Thank you! Any questions?